# Van’s Aircraft RV-8A

# Pilot’s Operating Handbook

4X-OAA

S/N 80295

Owners:

Ariel Arielly – Primary Builder

Eli Liberty – Primary Builder

Haim Raveh – Primary Builder

Israel Komet

Menachem Katz

Michael Verbin

Rev: C.5, 01 Jan. 2016

Rev. C.5

List of effective pages

| Page | Rev. | Effective Date | Page | Rev. | Effective Date |
| --- | --- | --- | --- | --- | --- |
| 1 | B.2 | 15/12/2011 | 21 | B.2 | 01/12/2011 |
| 2 | B.2 | 15/12/2011 | 22 | B.2 | 15/12/2011 |
| 3 | B.2 | 15/12/2011 | 23 | B.1 | 01/12/2011 |
| 4 | B.2 | 15/09/2012 | 24 | B.2 | 15/12/2011 |
| 5 | B.1 | 01/12/2011 | 25 | B.1 | 01/12/2011 |
| 6 | B.1 | 01/12/2011 | 26 | B.2 | 15/12/2011 |
| 7 | B.1 | 01/12/2011 | 27 | B.2 | 15/12/2011 |
| 8 | B.1 | 01/12/2011 | 28 | C.5 | 01/01/2016 |
| 9 | C.4 | 15/05/2015 | 29 | C.1 | 01/01/2013 |
| 10 | C.1 | 01/01/2013 | 30 | C.5 | 01/03/2016 |
| 11 | B.2 | 15/12/2011 | 31 | B.2 | 15/12/2011 |
| 12 | B.2 | 15/12/2011 | 32 | B.2 | 13/03/2012 |
| 13 | C.1 | 01/01/2013 | 33 | C.5 | 01/01/2016 |
| 14 | B.2 | 15/12/2011 | 34 | C.5 | 01/01/2016 |
| 15 | B.2 | 15/12/2011 | 35 | B.2 | 15/12/2011 |
| 16 | B.2 | 15/12/2011 | 36 | B.2 | 15/12/2011 |
| 17 | B.2 | 15/12/2011 | 37 | B.2 | 15/12/2011 |
| 18 | B.1 | 01/12/2011 | 38 | B.1 | 01/12/2011 |
| 19 | B.1 | 26/10/2011 | 39 | B.1 | 01/12/2011 |
| 20 | B.2 | 15/12/2011 | 40 | B.1 | 01/12/2011 |

Rev. C.4

| Page | Rev. | Effective Date | Page | Rev. | Effective Date |
| --- | --- | --- | --- | --- | --- |
| 41 | B.2 | 15/12/2011 | 69 | B.2 | 15/12/2011 |
| 42 | B.1 | 01/12/2011 | 70 | B.2 | 15/09/2012 |
| 43 | B.1 | 01/12/2011 | 71 | B.1 | 01/12/2011 |
| 44 | B.1 | 01/12/2011 | 72 | B.1 | 01/12/2011 |
| 45 | B.1 | 01/12/2011 | 73 | B.2 | 15/12/2011 |
| 46 | B.1 | 01/12/2011 | 74 | B.1 | 01/12/2011 |
| 47 | B.2 | 15/12/2011 | 75 | B.2 | 15/09/2012 |
| 48 | B.1 | 01/12/2011 | 76 | B.2 | 15/09/2012 |
| 49 | B.1 | 01/12/2011 | 77 | B.2 | 15/09/2012 |
| 50 | B.1 | 01/12/2011 | 78 | B.2 | 15/09/2012 |
| 51 | B.2 | 15/12/2011 | 79 | B.2 | 15/09/2012 |
| 52 | B.1 | 01/12/2011 | 80 | B.2 | 15/09/2012 |
| 53 | B.2 | 15/12/2011 | 81 | B.2 | 15/09/2012 |
| 54 | B.2 | 15/12/2011 | 82 | B.2 | 15/09/2012 |
| 55 | B.1 | 01/12/2011 | 83 | B.2 | 15/09/2012 |
| 56 | B.2 | 09/09/2012 | 84 | B.2 | 15/09/2012 |
| 57 | B.1 | 01/12/2011 | 85 | B.2 | 15/09/2012 |
| 58 | B.1 | 01/12/2011 | 86 | C4 | 15/05/2015 |
| 59 | B.1 | 01/12/2011 | 87 | B.2 | 15/09/2012 |
| 60 | B.1 | 01/12/2011 | 88 | B.2 | 15/12/2011 |
| 61 | C.1 | 01/01/2013 | 89 | B.2 | 01/01/2012 |
| 62 | C.1 | 01/01/2013 | 90 | C.2 | 29/01/2013 |
| 63 | C.1 | 01/01/2013 | 91 | B.2 | 15/09/2012 |
| 64 | C.1 | 01/01/2013 | 92 | B.2 | 15/09/2012 |
| 65 | C.1 | 01/01/2013 | 93 | B.2 | 15/09/2012 |
| 66 | C.1 | 01/01/2013 | 94 | C.3 | 01-04-2013 |
| 67 | C.1 | 01/01/2013 | 95 | N.A |  |
| 68 | B.1 | 01/12/2011 | 96 | N.A |  |

Rev. B.2

TABLE OF CONTENTS

Symbols, Abbreviations and Terminology . . . . . . . . . . . .           SECTION I

SPECIFICATIONS - PERFORMANCE . . . . . . . . . . . . . . . . . . . . . . . 	SECTION 1

PERFORMANCE . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .. . . . . . . . . 	SECTION 2

LIMITATIONS  .  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 	SECTION 3

3D ILLUSTRATION  . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . 	SECTION 4

WEIGHT & BALANCE . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  	SECTION 5

NORMAL PROCEDURES . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  	SECTION 6

EMERGENCY PROCEDURES. . . . . . . . . . . . . . . . . . . . . . . . . . . . . .	SECTION 7

AIRPLANE & SYSTEMS DESCRIPTIONS . . . . . . . . . . . . . . . . . . . . 	SECTION 8

AIRPLANE HANDLING, SERVICE & MAINTENANCE  . . . . . . . . . . 	SECTION 9

Reserved For Additional Data. . . . . . . . . . . . . . . . . . . . . . . . . . . . . 	SECTION 10

APPENDIXES . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . . .  	SECTION 11

This aircraft is certified in the Amateur-Built category. The regulations governing the Amateur-built category contain only very limited performance requirements and no flight characteristics requirements. By virtue of its Amateur-built status, all persons entering this aircraft do so at their own risk.

Rev. B.1

Symbols, Abbreviations and Terminology

- General Airspeed Terminology and Symbols

| KCAS | Knots Calibrated Airspeed - indicated airspeed corrected for position and instrument error and expressed in knots. Knots calibrated airspeed is equal to KTAS in standard atmosphere at sea level. |
| --- | --- |
| KIAS | Knots Indicated Airspeed – the speed shown on the airspeed indicator and expressed in knots. |
| KTAS | Knots True Airspeed – The airspeed expressed in knots relative to undistributed air which is KCAS corrected for altitude and temperature. |
| VA | Maneuvering Speed – The maximum speed at which you may use abrupt control travel. |
| VFE | Maximum Flap Extended Speed – The highest speed permissible with wing flaps in a prescribed extended position. |
| VNO | Maximum Structural Cruising Speed – The speed that should not be exceeded except in smooth air, then only with caution. |
| VNE | Never Exceed Speed – The speed limit that may not be exceeded at any time. |
| VS | Stalling Speed - The minimum steady flight speed at which the airplane is controllable. |
| VSO | Stalling Speed in Landing Configuration – The minimum steady flight speed at which the airplane is controllable in the landing configuration at the most forward center of gravity. |
| VX | Best Angle-of-Climb Speed – The speed which results in the greatest gain of altitude in a horizontal distance. |
| VY | Best Rate-of-Climb Speed – The speed which results in the greatest gain of altitude in a given time. |

Rev. B.1

- Meteorological Terminology

| OAT | Outside Air Temperature – The free air static temperature. It is expressed in either degrees Celsius or degrees Fahrenheit. |
| --- | --- |
| Standard Temperature | Standard Temperature – Is 15°C at sea level pressure altitude and decreases by 2°C for each 1000’ feet of altitude. |
| Pressure Altitude | Pressure Altitude – The altitude read from the altimeter when the altimeter’s barometric scale has been set to 29.92 inches of Mercury (1013mb). |
| Density Altitude | Density Altitude - The altitude in the International Standard Atmosphere that has the same air density as the air being evaluated. |

- Engine Power Terminology

| BHP | Brake Horsepower – The power developed by the engine. |
| --- | --- |
| RPM | Revolutions Per Minute – Engine speed. |
| MP | Manifold Pressure – Air pressure measured in the engine’s induction system and expressed in inches of mercury (Hg). |

- Airplane performance and flight planning terminology

| Demonstrated Cross Wind Velocity | Demonstrated Cross Wind Velocity – The velocity of the cross wind component for which adequate control of the airplane during take-off and landing was actually demonstrated during certification tests. The value shown is not considered to be limiting. |
| --- | --- |
| Usable Fuel | Usable Fuel – The fuel available for flight planning. |
| Unusable Fuel | Unusable Fuel – The quantity of fuel that can not be safely used in flight. |
| GPH | Gallon Per Hour – the amount of fuel (in gallons) consumed per hour. Rev. B.1 |
| NMPG | Nautical Miles Per Gallon – The distance (in nautical miles) which can be expected per gallon of fuel consumed at a specific engine power setting and/or flight configuration. |
| g | G - The acceleration due to gravity. |

- Weight and balance terminology

| Reference Datum | Reference Datum – An imaginary vertical plane from which all horizontal distances are measured for balance purposes. |
| --- | --- |
| Station | Station – A location along the airplane fuselage given in terms of the distance from the reference datum. |
| Arm | Arm – The horizontal distance from the reference datum to the centre of gravity (CG) of an item. |
| Moment | Moment – The product of the weight of an item multiplied by its arm. |
| Centre of Gravity (CG) | CG – The point at which an airplane, or equipment, would balance if suspended. Its distance from the reference datum is found by dividing the total moment by the total weight of the airplane. |
| CG Arm | Centre of Gravity Arm – The arm obtained by adding the airplane’s individual moments and dividing the sum by the total weight. |
| CG Limits | Centre of Gravity Limits – The extreme centre of gravity locations within the airplane must be operated at a given weight. |
| Standard Empty Weight | Standard Empty Weight – The weight of a standard airplane, including unusable fuel, full operating fluids and full engine oil. |
| Basic Empty Weight | Basic Empty Weight – The standard empty weight plus the weight of optional equipment. |
| Useful Load | Useful Load – The difference between the ramp weight and the basic empty weight. |
| MRW | Maximum Ramp Weight – The maximum weight approved for ground maneuver. (It includes weight of start, taxi and run-up fuel). Rev. B.1 |
| MTW | Maximum Takeoff Weight – The Maximum weight approved for the start of the takeoff run. |
| MLW | Maximum Landing Weight – The maximum weight approved for the landing touchdown. |
| Tare | Tare – The weight of chokes, blocks, stands, etc. used when weighing an airplane, and is included in the scale readings. Tare is deducted from the scale reading to obtain the actual (net) airplane weight. |

Rev. C.4

Section 1

SPECIFICATIONS

(All performance data is presented at typical Israeli Atmosphere - 28ºC and 70% RH)

| Dimensions |  |  |
| --- | --- | --- |
|  | Span | 24’ 0” (7.32m) |
|  | Length | 20’10” (6.35m) |
|  | Height | 7’ 4” (2.24m) |
|  | Wing Area | 116 sq ft (10m2) |
| SPEED: |  |  |
|  | Maximum at Sea Level | 200 Kt IAS |
|  | Cruise, 75% Power at 8,000 Ft | 163 Kt IAS |
| RANGE | (includes 3 gal. for taxi, takeoff & climb): |  |
|  | 75% @ 8000’ , no reserve | 608 nm (1126 km) |
|  | 55% @ 8000’ no reserve | 739 nm (1368 km) |
|  | 75% @ 8000’, one hour (8 gal) reserve | 446 nm (825 km) |
|  | 55% @ 8000’, one hour (8 gal) reserve | 594 nm (1100 km) |
| RATE OF CLIMB | AT SEA LEVEL | 1,800 FPM |
| SERVICE CEILING |  | 24,500 FT |
| TAKEOFF Distance |  | 535 Ft (165m) |
| LANDING Distance |  | 500 Ft (153m) |
| STALL SPEED (IAS): | Flaps Up, Power Off | 60 Kt |
|  | Flaps Down, Power Off | 55 Kt |
|  |  | Rev. C.1 |
| WEIGHTS: | MAXIMUM WEIGHT (Normal Category & hard paved runways)) | 1900 Lbs (862kg) |
|  | MAXIMUM WEIGHT (Non paved runways) | 1800 Lbs (816kg) |
|  | EMPTY WEIGHT | 1138 Lbs (516.2kg) |
|  | MAXIMUM USEFUL LOAD | 762 Lbs (346kg) |
|  | BAGGAGE ALLOWANCE | 125 Lbs (56.7kg) per CG limits |
| WING LOADING | (gross weight / wings area) | 16.4 lb/ft2 |
|  | Positive G limit (See appendix 11.5) | + 6 g (5g) |
|  | Negative G limit (See appendix 11.5) | - 3 g (2g) |
| POWER LOADING | (gross weight / engine HP) | 10.55 lb/hp |
| FUEL: | Capacity | 42 Gal Total (159 lit) |
|  | Unusable | 1 Gal Total (3.8 8lit) |
|  | Type | 100LL Avgas or 95 Octane MoGas |
| OIL | Capacity | Normal operating 7 Qts (8 Qts max for long range flights) |
|  | Type | SAE20W50 Mil-L-22851 or SAEJ1899 Ashless Dispersant |
| ENGINE | Lycoming 180HP model | XIO-360-M1B |
|  | Rated hors-power | 180 (134.2kW) |
|  | Rated speed (RPM) | 2700 |
|  | Bore / Stroke, inches | 5.125 / 4.375 |
|  | Displacement, cubic inches | 361.0 |
|  | Compression ratio | 8.5:1 |
|  |  | Rev. B.2 |
|  | Firing order | 1-3-2-4 |
| PROPELLER | Harzel Model: | 72" dia. C/S C2YR-1BF/F7496-2 |

##### Rev. B.2

##### This page left Blank intentionally

##### Rev. C.1

##### Section 2

##### Performance

Cruise Performance at 3,000’and below (OAT = 30°C, Mixture Adjusted(*)):

| IAS (/Kt) | RPM | MAP | Fuel Flow (gph) | % Power |
| --- | --- | --- | --- | --- |
| 134 | 2100 | 20.7" | 7.4 | 55 (99HP) |
| 138 | 2200 | 20.1” |  |  |
| 143 | 2300 | 19.6” |  |  |
| T.B.D | 2100 | 23.0" | 8.8 | 65 (117HP) |
| T.B.D | 2200 | 22.4" |  |  |
| T.B.D | 2300 | 21.8" |  |  |
| T.B.D | 2200 | 24.8" | 10.0 | 75 (135HP |
| T.B.D | 2300 | 24.2" |  |  |
| T.B.D | 2400 | 23.7" |  |  |

Cruise Performance at 8,000’ (Israeli typical OAT, Mixture Adjusted(*)):

| IAS (/Kt) | RPM | MAP | Fuel Flow (gph) | % Power |
| --- | --- | --- | --- | --- |
| T.B.D | 2100 | 19.5" | 7.4 | 55 (99HP) |
| T.B.D | 2200 | 18.9" | 7.4 |  |
| T.B.D | 2300 | 18.5" | 7.4 |  |
| T.B.D | 2100 | 21.8" | 8.8 | 65 (117HP) |
| T.B.D | 2200 | 22.2" | 8.8 |  |
| T.B.D | 2300 | 20.7" | 8.8 |  |
| T.B.D | 2200 | --- | 10.0 | 75 (135HP |
| T.B.D | 2300 | --- | 10.0 |  |
| T.B.D | 2400 | 22.5" | 10.0 |  |

(*) Fuel flow is based on Peak EGT enriched by 50 degrees down.

Range at 8,000’ , No Wind:

- All range calculations include 3 gal. for engine start, taxi, takeoff and climb.

| One hour (8 gal.) reserve: |  |  |
| --- | --- | --- |
|  | 75% Power | T.B.D |
|  | 65% Power | T.B.D |
|  | 55% Power | T.B.D |

Rev. B.2

This page left Blank intentionally

Rev. B.2

Section 3

LIMITATIONS

| SPEED | IAS (Kt) | REMARKS |
| --- | --- | --- |
| VNE | Never Exceed Speed | 200 | Do not exceed this speed in any operations. |
| VNO | Maximum Structural Cruising Speed | 170 | Exceed this speed only in smooth air. |
| VA | Maneuvering Speed | 123 | Do not make full control movements above this speed. Full elevator deflection will result in a 6g load at this speed. |
| VFE | Maximum Flap Extended Speed | 95 | Do not exceed this speed with flaps down |
| Vy | Best Rate of Climb | 85 |  |
| Vx | Best Angle of Climb | 75 |  |
| Vs | Stall Speed Clean | 54 |  |
| Vso | Stall Speed Landing Configuration | 51 |  |

AIRSPEED INDICATOR MARKINGS

| MARKING | IAS VALUE (Kt) | SIGNIFICANCE |
| --- | --- | --- |
| White Arc | 50 – 87 | Full Flap Operating Range. Lower limit is Vso. Upper limit is maximum speed with flaps extended |
| Green Arc | 50 – 168 | Normal Operating Range. Lower limit is Vs. Upper limit is maximum structural cruising speed |
| Yellow Arc | 168 – 200 | Caution range, to be flown only in calm or light turbulence condition. |
| Red Line | 200 | Maximum speed for all operations |

Rev. B.2

Aerobatic Entry Speeds

| Maneuvering | Airspeed Entry |
| --- | --- |
| Loops, Horizontal Eights | 122 – 165 Kt |
| Immelman Turns | 130 – 165 Kt |
| Ailerons Rolls, Barrel Rolls | 104 – 165 Kt |
| Snap Rolls | 70 – 96 Kt |
| Vertical Rolls | 156 – 165 Kt |
| Split-S | 87 – 96 Kt |
| Spin | Low speed |

"Know your airplane, know it well, know its limitations, and above all – know your own limitations" (Bob Hoover)

Fig. 3.1 -Take-Off Distance & Rate of Climb Performance

Rev. B.2

This page left Blank intentionally

Rev. B.1

Section 4 - 3D ILLUSTRATION

Fig. 4.1 – 3D Views

Rev. B.1

##### Fig. 4.2 – Cockpit and luggage compartments dimensions

##### Rev. B.2

##### Section 5 - WEIGHT AND BALANCE

| Maximum Weights: |
| --- |
|  | Aerobatic Category (See Appendix 11.5) | 1550 Lbs (703kg) |
|  | Normal Category (See Appendix 11.5) | 1900 Lbs (816kg) |
| Arms: |  |  |
|  | Datum | 70 inches forward of wing leading edge (L.E.) |
|  | Design C.G. Range | 15% to 29% of wing chord |
|  |  | 8.7” to 16.8” from L.E |
|  |  | 78.7” to 86.82” aft of Datum |
|  | Aerobatic Aft. CG Limit | 26.5 % of wing cord |
|  |  | 15.3" from LE |
|  |  | 85.3" aft of Datum |
|  | Wing L.E | 70 inches aft of datum |
|  | Main wheel right | 94.06” aft of datum |
|  | Main wheel left | 94.06” aft of datum |
|  | Nose wheel | 34.55” aft of datum |
|  | Fuel | 80.00” aft of datum |
|  | Pilot | 91.78” aft of datum |
|  | Passenger | 119.12” aft of datum |
|  | Forward Baggage | 58.51” aft of datum |
|  | Aft Baggage (Floor) | 138.00” aft of datum |
|  | Aft Baggage (Shelf) | 152.91" aft of Datum |

Fig. 5.1 – Arms Stations for Empty W&B

Rev. B.2

Aircraft weights empty in level flight attitude. (Includes 6 qts. of oil & unusable fuel)

| Location | Weight | Arm | Moment |
| --- | --- | --- | --- |
| Right Wheel | 408 | 94.06 | 38376 |
| Left Wheel | 438 | 94.06 | 41198 |
| Nose Wheel | 292 | 34.55 | 10089 |
| Total | 1138 |  | 89663.36 |
| Empty CG |  | 78.79" aft of datum |  |

##### Weight & Balance Data Calculation (Sample):

| # |  | Weight | Arm | Moment (= Arm x Weight) |
| --- | --- | --- | --- | --- |
| 1 | Aircraft | 1138 | 78.79 | 89663.36 |
| 2 | Fuel (6lbs/gal) |  | 80.00 |  |
| 3 | Pilot |  | 91.78 |  |
| 4 | Passenger |  | 119.12 |  |
| 5 | Fwd Baggage |  | 58.51 |  |
| 6 | Aft Baggage |  | 138.00 |  |
| 7 | Total | = sum (Weight 1 to Weight 6) | CG = Total Moment / Total Weight | = sum (Moment 1 to Moment 6) |

CG allowable range = 78.70 to 86.82 in aft of datum

Rev. B.2

Fig. 5.2 - CG envelope

Fig. 5.3 – CG Moment Envelope

Rev. B.1

WEIGHT AND BALANCE DATA (Samples)

| Table No. 1 - Pilot and Pax (Heavy) |  | Table No. 2 - Full Baggage no Pax |
| --- | --- | --- |
| Empty Weight | 1138 | 78.79 | 89663 |  | Empty Weight | 1138 | 78.79 | 89663 |
| Fuel | 276 | 80.00 | 22080 |  | Fuel | 276 | 80.00 | 22080 |
| Pilot | 190 | 91.78 | 17438 |  | Pilot | 190 | 91.78 | 17438 |
| Passenger | 170 | 119.12 | 20250 |  | Passenger | 0 | 119.12 | 0 |
| FWD Baggage | 25 | 58.51 | 1463 |  | FWD Baggage | 90 | 58.51 | 5266 |
| AFT Baggage Floor | 0 | 138.00 | 0 |  | AFT Baggage Floor | 80 | 138.00 | 11040 |
| AFT Baggage Shelf | 0 | 152.91 | 0 |  | AFT Baggage Shelf | 25 | 152.91 | 3823 |
| Total | 1799 |  | 150894 |  | Total | 1799 |  | 149310 |
| CG Arm |  | 83.88 |  |  | CG Arm |  | 83.00 |  |
| Table No. 3 - Same as Table No. 1 - end of Flight |  | Tabel No. 4 - Same as Table No. 2 - end of Flight |
| Empty Weight | 1138 | 78.79 | 89663 |  | Empty Weight | 1138 | 78.79 | 89663 |
| Fuel | 24 | 80.00 | 1920 |  | Fuel | 24 | 80.00 | 1920 |
| Pilot | 190 | 91.78 | 17438 |  | Pilot | 190 | 91.78 | 17438 |
| Passenger | 170 | 119.12 | 20250 |  | Passenger | 0 | 119.12 | 0 |
| FWD Baggage | 25 | 58.51 | 1463 |  | FWD Baggage | 90 | 58.51 | 5266 |
| AFT Baggage Floor | 0 | 138.00 | 0 |  | AFT Baggage Floor | 80 | 138.00 | 11040 |
| AFT Baggage Shelf | 0 | 152.91 | 0 |  | AFT Baggage Shelf | 25 | 152.91 | 3823 |
| Total | 1547 |  | 130734 |  | Total | 1547 |  | 129150 |
| CG Arm |  | 84.51 |  |  | CG Arm |  | 83.48 |  |
| Table No. 5 - Pilot and Pax (Light) |  | Table No. 6 - Same as Table No. 5 - end of Flight |
| Empty Weight | 1138 | 78.79 | 89663 |  | Empty Weight | 1138 | 78.79 | 89663 |
| Fuel | 276 | 80.00 | 22080 |  | Fuel | 24 | 80.00 | 1920 |
| Pilot | 120 | 91.78 | 11014 |  | Pilot | 120 | 91.78 | 11014 |
| Passenger | 170 | 119.12 | 20250 |  | Passenger | 170 | 119.12 | 20250 |
| FWD Baggage | 50 | 58.51 | 2926 |  | FWD Baggage | 50 | 58.51 | 2926 |
| AFT Baggage Floor | 45 | 138.00 | 6210 |  | AFT Baggage Floor | 45 | 138.00 | 6210 |
| AFT Baggage Shelf | 0 | 152.91 | 0 |  | AFT Baggage Shelf | 0 | 152.91 | 0 |
| Total | 1799 |  | 152143 |  | Total | 1547 |  | 131983 |
| CG Arm |  | 84.57 |  |  | CG Arm |  | 85.32 |  |

Rev. B.2

This page left Blank intentionally

Rev. B.1

Section 6 - NORMAL PROCEDURES

##### PREFLIGHT INSPECTION

Fig. 6.1 – Pre-Flight Inspection sequence

| [1] CABIN |  |  |
| --- | --- | --- |
| 1 | Documentation | Available In Airplane: Airworthiness Certificate Registration Radio Station. Operating Limitations Weight and Balance information |
| 2 | Aeronautical Charts | CURRENT AND APPROPRIATE TO FLIGHT |
| 3 | Seat Belt Securing Control Stick | RELEASE |
| 4 | Ignition Switches | OFF |
| 5 | Avionics Switch | OFF |
| 6 | Master Switch | ON |
| 7 | Fuel Quantity | CHECK QUANTITY -- VERIFY ENGINE MONITOR RESET |
| 8 | Master Switch | OFF |

Rev. B.2

WARNING

When turning ON the master switch, using an external power source, or pulling the propeller through by hand, treat the propeller as if the ignition switches were ON.  Do not stand, nor allow anyone else to stand, within the arc of the propeller, since a loose or broken wire, or a component malfunction, could cause the propeller to rotate.

| [2] STATIC PORT |  |
| --- | --- |
| 1 | Static inlet | CHECK for blockage |

| [3] EMPENNAGE |  |
| --- | --- |
| 1 | Tail Tie-Down | DISCONNECT |
| 2 | Control Surfaces | CHECK freedom of movement and Bearings |

| [4] STATIC PORT |  |
| --- | --- |
| 1 | Static inlet | CHECK for blockage |

| [5, 6, 7 & 8] RIGHT WING |
| --- |
| 1 | Flap | CHECK security |
| 2 | Aileron | CHECK freedom of movement and Bearings |
| 3 | Nav. and Strobe Light | CHECK condition |
| 4 | Landing Light | CHECK condition |
| 5 | Wing Tie-Down | DISCONNECT |
| 6 | Fuel Quantity | CHECK VISUALLY |
| 7 | Fuel Filler Cap | SECURE!!! |
| 8 | Fuel Drain | Drain and Check – NO WATER! |
| 9 | Main Wheel Tire | CHECK for proper inflation |
| 10 | Chock | REMOVE |
| 11 | Right Wing Tank | Check General Status |

Rev. B.2

| [9] NOSE |  |
| --- | --- |
| 1 | Engine Oil Level | CHECK, do not operate with less than 5 quarts. Check oil color. For local flights not more than 7 Qts. |
| 2 | Propeller and Spinner | CHECK for nicks and security |
| 3 | Cowl Hinge Pins and Cam-locks | CHECK for security |
| 4 | Air Inlet | Remove two red plugs. CHECK for restrictions |
| 5 | Air Filter | Clean and not blocked |
| 6 | Nose Wheel Tire | CHECK for proper inflation |
| 7 | Fuel Tank Vents | CHECK for blockage |

| [10, 11, 12 & 13] LEFT WING |
| --- |
| 1 | Main Wheel Tire | CHECK for proper inflation |
| 2 | Chock | REMOVE |
| 3 | Left Wing Tank | Check General Status |
| 4 | Fuel Quantity | CHECK VISUALLY |
| 5 | Fuel Filler Cap | SECURE |
| 6 | Fuel Drain | Drain and Check – NO WATER! |
| 7 | Pitot Tube Cover | REMOVE and check for Pitot blockage |
| 8 | Wing Tie-Down | DISCONNECT |
| 9 | Taxi Light | CHECK condition |
| 10 | Nav. and Strobe Lights | CHECK condition |
| 11 | Aileron | CHECK freedom of movement and Bearings |
| 12 | Flap | CHECK security |

Rev. C.5

| BEFORE STARTING ENGINE |
| --- |
| 1 | Preflight Inspection | COMPLETE |
| 2 | Seat Belts and Shoulder Harnesses | ADJUST and LOCK. Lock rear harness! Check back seat cushions and secure. |
| 3 | Canopy | OPEN or Closed and secur. depending on weather |
| 4 | Fuel Selector Valve | LEFT TANK |
| 5 | Avionics and Electrical | Master Avionics Switch – OFF |
| 6 | Brakes | Apply |
| 7 | Prop | CLEAR |

| STARTING ENGINE |
| --- |
| 1 | Master Switch | ON |
| 2 | Strobe | ON if required |
| 3 | Mixture | Full forward |
| 4 | Prop | Full forward |
| 5 | Throttle | Full forward |
| 6 | Boost Pump | ON (2 to 3 seconds) then OFF |
| 7 | Throttle | Full aft. then OPEN ¼ forwards |
| 8 | Propeller Area | CLEAR |
| 9 | Ignition Switches | ON (Both) |
| 10 | Starter Button | PRESS |
| 11 | Mixture (Cold Engine) | Leave OPEN |
| 11 | Mixture (Hot Engine) | Close. When engine starts, open slowly to Full Rich. |
| 12 | Throttle | ADJUST to 900 -1000 rpm |
| 13 | Oil Pressure | CHECK 25+ psi at idle |
| 14 | Alternator | ON |
| 15 | Avionics | ON |
| 16 | Radio | Control Tower |

#### Note:

Any ground check that requires full throttle operation must be limited to three minutes, or less if the cylinder head temperature should be exceed the maximum as stated in the engine manual.

Rev. C.1

| BEFORE TAKEOFF (Run-Up) |
| --- |
| 1 | Brakes | Apply |
| 2 | Flight Controls | FREE and CORRECT |
| 3 | Dynon EFIS | SET (ALT & Compass) |
| 4 | Altimeter (Mechanical) | Airport Pressure |
| 5 | Fuel Selector Valve | DESIRED TANK |
| 6 | Elevator and Aileron Trim | Take-Off |
| 7 | Mixture | Full forward |
| 8 | Prop | Full forward |
| 9 | Throttle | 1800 rpm |
| 10 | Magnetos RPM Drop | Check (Max 175, difference not more than 50 between them) |
| 11 | Prop | Full Course (Max 500 RPM drop) |
| 12 | Engine Instruments | CHECK (Green) |
| 13 | Throttle | IDLE then 900 - 1000 rpm |
| 14 | Radios | Request Clearance |
| 15 | Transponder | ON - STBY |
| 16 | Check Flight Timer in EFIS |  |
| 17 | Canopy | Latch & SECURE |

| NORMAL TAKEOFF |
| --- |
| 1 | Lights (Strobe, Position & Land) | ON if required |
| 2 | Boost Pump | ON |
| 3 | Wing Flaps | Down 1 Green LED |
| 4 | Mixture | Full forward |
| 5 | Prop | Full forward |
| 6 | Throttle | Full forwards (2700 rpm) |
| 7 | Elevator Control | LIFT NOSE WHEEL (at 50 Kt IAS) |
| 8 | Climb Speed | 100 Kt IAS |
| 9 | Wing Flaps | After reaching 300ft AGL - Up |
| 10 | Throttle & Prop | Establish 22² to 23² Setting as required |
| 11 | Mixture | After stable climbing speed achieved – lean to best power (Peak EGT minus 50 degrees F) |
| 12 | Boost Pump | OFF |

Rev. C.1

| SHORT FIELD TAKEOFF (Not recommended) |
| --- |
| 1 | Boost Pump | ON |
| 2 | Wing Flaps | 8 Deg (2 Green LEDs) |
| 3 | Brakes | APPLY |
| 4 | Mixture | Full forward |
| 5 | Prop | Full forward |
| 6 | Throttle | Full forward |
| 7 | Stick | BACK |
| 8 | Brakes | RELEASE |
| 9 | Initial climb Speed | 70 Kt IAS (Vy) |
| 10 | After reaching 300ft AGL – speed 100 Kt, Flaps Up and fuel pump - OFF |

| ENROUTE CLIMB |
| --- |
| 1 | Airspeed | 100 – 115 Kt IAS |
| 2 | Throttle | 23 in Hg |
| 3 | Prop | 2300 RPM |
| 4 | Mixture | lean to best power (Peak EGT minus 50 degrees F) |
| 5 | Transponder | ALT |

| CRUISE | (3000ft @ 65% Power) » 140Kt IAS |
| --- | --- |
| 1 | Throttle | 22 in Hg |
| 2 | Prop | 2200 RPM |
| 3 | Mixture (!!!) | lean to best power (Peak EGT minus 50 degrees F) |

| LANDING |  |  |
| --- | --- | --- |
| 1 | Fuel Selector | To fullest tank |
| 2 | Boost pump | On |
| 3 | Speed | Slow to 80 Kt IAS, 70 at final |
| 4 | Flaps | as needed |
| 5 | Mixture | Full forward |
| 6 | Prop | Full forward |
| 7 | Landing Lights | ON |

##### Rev. B.2

| AFTER LANDING |
| --- |
| 1 | Boost pump | OFF |
| 2 | Wing Flaps | Full Down (used to break speed while taxing) |
| 3 | Transponder | OFF |

| ENGINE SHUTDOWN |
| --- |
| 1 | Flaps | UP |
| 2 | Master Switch (BAT) | OFF |
| 3 | Throttle | 1000 RPM |
| 4 | Mixture | Full Backwards |
| 5 | Ignition Switches | OFF |

| SECURING AIRCRAFT |
| --- |
| 1 | Wheel Chocks | INSTALL |
| 2 | Wing & Tail Tie-Down | INSTALL AS REQUIRED |
| 3 | Pitot Tube Cover | INSTALL AS REQUIRED |
| 4 | Cockpit | CLEAN AND SECURE |
| 5 | Master and Electrical Switches | Check - OFF |
| 6 | Canopy | Close, Secured and lock. |
| 7 | Engine air intake | Insert two red plugs |
| 8 | Aircraft | Cover |
| 9 | Prop & Stick | Chain, Lock |

Rev. B.2

This page left Blank intentionally

Rev. C.5

Section 7 - EMERGENCY PROCEDURES

! Remember - Always continue to fly the aircraft !

| AIRSPEEDS FOR EMERGENCY OPERATIONS |
| --- |
|  | Maximum Glide Speed (See Appendix 11.6 for glide performance) | 95 Kt IAS |
|  | Maneuvering Speed (Va) | 100 Kt IAS |
| Engine Failure After Takeoff: |  |
|  | Wing Flaps Up | 70 Kt IAS |
|  | Wing Flaps Down | 61 Kt IAS |

| ENGINE FAILURES |
| --- |
| ENGINE FAILURE DURING TAKEOFF RUN |
| 1 | Throttle | IDLE |
| 2 | Brakes | APPLY |
| 3 | Wing Flaps | Down |
| 4 | Ignition Switches | OFF |
| 5 | Master Switch | OFF |

| ENGINE FAILURE IMMEDIATELY AFTER TAKEOFF Keep Flying! |
| --- |
| 1 | Airspeed | 70 Kt IAS |
| 2 | Fuel Selector Valve | OFF |
| 3 | Ignition Switches | OFF |
| 4 | Wing Flaps | AS REQUIRED |
| 5 | Master Switch | OFF |

| ENGINE FAILURE DURING FLIGHT Keep Flying! |
| --- |
| 1 | Airspeed | 95 Kt IAS |
| 2 | Landing Area | Look for |
| 3 | Fuel Selector Valve | SWITCH TANK |
| 4 | Boost pump | ON |
| 5 | Mixture | Full rich |
| 6 | Throttle | Full back then slowly forward for start engine |
| If engine fails to start: |  |
| 7 | Fuel Valve | Close!!! |
| 8 | Ignition Switches | OFF |
| 10 | Landing | Initiate and Perform forced landing: |
| 11 | Radio | Report |
| 12 | Flaps | As required |
| 13 | Master Switch | OFF |

| FIRES |
| --- |
| DURING START ON GROUND |
| If engine starts: |  |
| 1 | Cranking | CONTINUE, to get a start which would suck the flames and accumulated fuel through the servo and into the engine |
| 2 | Power | 1700 RPM for a few seconds |
| 3 | Engine | SHUTDOWN and inspect for damage |
| If engine fails to start: |  |
| 1 | Throttle | FULL OPEN |
| 2 | Cranking | CONTINUE |
| 3 | Fire Extinguisher | OBTAIN |
| 4 | Engine | SECURE |

Rev. C.5

| ENGINE FIRE IN FLIGHT Keep Flying! |
| --- |
| 1 | Fuel Selector Valve | OFF |
| 2 | Cabin Heat and Air | OFF |
| 3 | Landing | Initiate and Perform forced landing: |
| 4 | Radio | Report |
| 5 | Flaps | As required |
| 6 | Master Switch | OFF |

| ELECTRICAL FIRE IN FLIGHT Keep Flying! |
| --- |
| 1 | Master Switch | OFF |
| 2 | All Other Switches (except magneto) | OFF |
| 3 | Master Switch | ON |
| 4 | Turn ON switches to find short source | Leave defected switch OFF |
| 5 | Vents/ Cabin Air/ Heat | Open |
| 6 | Fire Extinguisher | ACTIVATE (if available) |

| CABIN FIRE |
| --- |
| 1 | Master Switch | OFF |
| 2 | Vents/ Cabin Air/ Heat | Open |
| 3 | Fire Extinguisher | ACTIVATE (if available) |

| WING FIRE |
| --- |
| 1 | Nav & Strobe Lights | OFF |
| 2 | Landing Lights | OFF |
| 3 | Pitot Heat | OFF |

Rev. B.2

| ELECTRICAL / ALTERNATOR FAILURE |
| --- |
| 1 | Electrical Equipment | ON, as required |
| 2 | Flight | TERMINATE as soon as practical, aircraft is on battery reserves only |

#### Rev. B.2

#### This page left Blank intentionally

#### Rev. B.1

#### Section 8 - AIRPLANE & SYSTEMS DESCRIPTIONS

8.1 AIRFRAME

The airframe is aluminum alloy construction except for steel components comprising: engine mount, landing gear, landing gear mounts, elevator control horns and other miscellaneous items. Fiber-glass parts are used for the tips of wings and tail fairings as well as for cowls, wheel fairings, empennage fairings and canopy skirt.

The aircraft's wings are conventionally configured with a NACA 23013.5 non laminar flow aerofoil.

8.2 COCKPIT LAYOUT

The aircraft's sitting arrangement is a "Tandem configuration" – Pilot at the front and Co-Pilot/Passenger at the rear.

The flight Data is all displayed by Dynon D-10 EFIS (Airspeed, AOA, Altimeter, VSI, Attitude (Artificial Horizon), Turn Indication, Ball and a Stable Magnetic Compass). Two conventional pneumatic instruments – ASI and a Sensitive Altimeter are located on both sides of the EFIS to serve as Back-Up.

The engine instruments are to the right side of flight instruments, and the avionics stack is to the left of the flight instruments (Figure 8.1a and 8.1b).

Fig. 8.1a – Flight Instruments                                 Fig. 8.1b – Engine Instruments

Rev. B.1

Switches that are normally mainly used on the ground are on a right sub-panel on the right to the instrument panel (Figure 8.2).

Switches that are normally used in flight are on the sub-panel to the left of the instrument panel (Figure 8.3).

Fig. 8.2 – Right side Sub-Panel

Fig. 8.3 – Left side Sub-Panel

The Throttle, Propeller control and Mixture are in a throttle quadrant mounted on the left cockpit wall below the instrument panel (Figure 8.4).

The Fuel selector and Fuel gauges and Fuel Low Level Warning Lamps are located at the left lower console is on a horizontal shelf on the lower, left side of the cockpit (Figure 8.5).

Fig. 8.5 – Fuel selector and Fuel Quantity Gauges

Rev. B.1

Voltmeter, Voltage Measurement Selector and Hobbes Counter, are located at the right lower console below the Electric Circuit Breakers panel (Figure 8.6) and (Figure 8.7)

Fig. 8.6 – Voltmeter and Selector                 Fig. 8.7 – Circuit-Breakers

The front stick grip contains controls for Pitch and Roll trim and PTT (Figure 8.8).

Fig 8.8 – Trim and PTT

Two Auxiliary Power Sockets, Rear and Front cabin Light Switches and two pairs of Headsets' sockets are located on the right wall of the cockpit (Figure 8.9).

Fig. 8.9 – Aux PWR sockets and Headsets and cabin light switches

Rev. B.2

A Pitch and Roll trim switch and PTT are also located on the Control Stick of the rear cockpit. The rear stick can be removed, if necessary, by removing a safety pin and disconnection of a D-Sub connector.

The rear seat has Throttle and Propeller Control levers which mounted on the left side wall (Figure 8.10).

Two push-button switches to control the radio channels in use (one for the GNS-430 and the second for the ICOM-A200) are located aft the rear Throttle quadrant to the left side wall. A safety two-position locked switch is used to disconnect the two push-buttons from the radios (Figure 8.11).

Fig 8.11 – Copilot's Avionics remote control panel

8.3 CANOPY

Canopy Latch - The canopy is latched by a handle and hook at the left front.

Although the handle may rotate and the hook may release if the handle is hit in flight, the air loads push the canopy forward, so there is no risk of it departing the aircraft.

8.4 ENGINE AND PROPELLER

The aircraft is powered by a Lycoming XI0-360-M1B four cylinder, direct drive, horizontally opposed engine rated at 180 HP at 2700 rpm. The engine is fitted with a 60 amp 14 volt main alternator, shielded magneto ignition, LASAR electronic ignition, Mechanical fuel pump, fuel injection and an alternate air induction system.

Rev. B.1

The exhaust system is all stainless with a crossover configuration and no mufflers.

One heat shroud provides cabin heat.

The propeller is a 74" Hartzell two-blade constant speed.

8.5 ENGINE CONTROLS

Engine controls consist of: Throttle, Propeller, Mixture, Alternate Air controls.

The throttle, propeller and mixture controls are in a throttle quadrant mounted on the left side of the front cockpit (and Throttle + Propeller Control on the left side of the passenger seat).

Alternate Air control is located on the left side above the Fuel gauges in adjacent to the Cabin Heat knob.

Rev. B.1

8.6 ENGINE Performance

The following curve summarizes the Fuel consumption, engine percentage power and CHT/EGT as function of fuel/air mixture.

Fig 8.11 Engine performances vs. fuel/air mixture setting

Rev. B.1

8.6 LANDING GEAR

The landing gear is of conventional tri-gear configuration with steel landing gear legs. The front wheel is a free swivel, un-controllable. Ground Direction control is done by the rudder at high-speed and by breaks at low speeds.

The main gear wheels are fitted with Cleveland 5:00 x 5 wheels and disk brakes.

The Nose-Wheel is "Matco" wheel system, 11 x 4.0 – 5 tire.

The braking system consists of two brakes attached to the rudder pedals operating individual Cleveland brake cylinders to each of the main landing wheels. The left and right brake cylinders share a common fluid reservoir installed on the top left front face of the fire wall.

Care must be taken to avoid applying brake pressure when using rudder on the ground.

Air pressure for the main wheels is 25psi and the front wheel is 32psi.

8.7 FLIGHT CONTROLS

Dual controls are fitted.

A pin at the base of the passenger control stick allows it to be removed without affecting the operation of the remaining controls. Elevator and ailerons are operated through a system of push rods. The rudder is operated by a cable system attached to the Pilot's adjustable rudder pedals and from the rear seat position by two pads connected to push rods that are connected to the rudder cables.

Pitch trim is by a tab on the right elevator actuated by an electric servo. Roll trim is by a spring system actuated by an electric servo. Pitch and roll trim are controlled by “Coolie Hat” switches on the pilot’s stick grip and on the rear stick. Trim positions are shown on LED indicators arranged in figure of "T" located on the upper left sub-panel (Figure 8.12). A "Two Place Trim Mixer" located under the pilot seat is used to enable control of the trim (both pitch and roll) from two "Coolie-hats" while preventing damage to the trim motors in case when two opposite inputs conflict between each other. The Trim Mixer gives priority to the firs input and ignores the other input.

Rev. B.1

Flaps are operated electrically and are continuously controlled by a switch mounted on the left sub-panel (Figure 8.13). LED's indicator indicates the Flap position.

Figure 8.12 – General view of the 2 Place Trim Mixer

Figure 8.13 – Flaps control lever and position indicator

8.9 FUEL SYSTEM (see fig. 8.14)

Fuel is stored in two 21gallons tanks secured to the leading edge structure with screws and plate nuts. Fuel drains are fitted to the lowest point of each and should be opened prior to the first flight of the day to check for sediment and water.

The left tank is fitted with an inverted fuel "Flop-Pickup", which is a weighted length of flexible line, with a fuel pickup at the loose end. This introduces additional failure modes for the left tank - the fuel pickup could get hung up inside the tank, or it could become disconnected at the front end. These failures would increase the amount of unusable fuel in the left tank by several gallons.

Rev. B.1

WARNING

Never assume that all fuel in the left tank is useable. There are 3/4 Gallon of un-used fuel in the right tank and 1 gallon in the left tank. The left tank must not be selected for take-off or landing unless there are at least 10 USG of fuel remaining. If it is planned to use most of the fuel on a flight, the left tank must be used to a low value first.

The fuel selector valve is located to the left of the pilot’s seat on the lower console.

An electric boost pump is fitted in case of failure of the engine-driven fuel pump and is also used during start, take off and landing, and when changing fuel tanks in flight. The boost pump is controlled by an ON/OFF toggle switch. The yellow boost pump lamp on the upper right instrument panel will illuminate when electrical power is applied to the boost pump.

The fuel filter is located on the left wall below the front baggage compartment. The electric boost pump is on the left side floor just after the fuel filter.

Gascolator and its drain valve are located just in front of the firewall to the left side of the lower engine cowling.

A fuel flow transducer is mounted between the Injection Fuel Air servo and the fuel spider. The fuel pressure transducer is mounted on the firewall and fed from the engine driven fuel pump.

Rev. B.2

Fig 8.14 – Fuel System Diagram

Rev. B.1

8.10 ELECTRICAL  SYSTEM (see Appendix A – Electrical Wiring diagram)

The electrical system is of conventional design employing two (parallel connected) 12V 20AH Acid, Sealed, maintenance free Battery as the Main electric source and a 12V 2AH back-up battery for the Dynon D-10 EFIS.

All Power supply is activated Through a Battery Master Solenoid controlled by the "Master – Battery" Switch on the right sub-panel.

All not essential electrical loads are fed from the Master Bus through circuit-breakers. A low voltage drop, Schottky diode feeds the Essential Equipment's Electric Bus. The Essential Bus might be fed through the "MLE (Minimum Load Essential Equipment) Switch" on the right sub-panel, in case of a total electrical power failure. The MLE switch is fed through an in-line fuse of 15A directly from the main battery. This fuse is located just to the right side of the battery tray behind the rear baggage compartment.

DC power to the Clock is fed through an in-line fuse of 1A connected directly to the main battery. This fuse is located in adjacent to the 15A MLE fuse.

The "Master – Alternator" switch, controls the output of the 60A rated alternator.  The alternator B-lead is routed thru a 70A in-line Fuse (located on the Engine side of the firewall) to the main Electric Bus.

A red Low Voltage warning lamp illuminate if the voltage drops below 12V.

The circuit breakers panel is accessible to the pilot on the right shelf just below the right sub-panel. Each electrical circuit is protected by a circuit breaker rated in accordance with the wires associated with this circuit.

The back-up battery for the Dynon is charged from the main bus through an in-line fuse rated 7A Slow-Blow. This fuse is monitored by a red LED which lit when the fuse is blown. The back-up battery's fuse and monitor LED are located on the front side of the circuit-breakers shelf.

The battery charge/discharge current is monitored by an Ammeter (located on the right sub-panel) which senses the current by a serial shunt element.

Rev. B.1

A Voltmeter (on the right lower console) enables voltage monitoring of several system junctions by a "Voltage Monitor Selector Switch".

The Starter Motor is activated by the "Starter" push-button, on the right sub-panel, which controls the starter solenoid located near the battery tray. Because of the huge amount of current required to crank the starter motor, there is no circuit protection for the 2AWG wire from the starter solenoid to the starter motor.

The negative pole of the battery (as well as all negative potential of the electrical system) is connected by a 2AWG wire to the aircrafts body in one point (under the floor at the left wall) as a "Star" configuration.

Lights, Electric Fuel Pump, Flaps and Pitot-Heat are all controlled by toggle switches on the left sub-panel.

DC power to the avionics (for each equipment separately) is switched by an Avionics Electronic Switch (attached to the rear side of the forward baggage compartment). This electronic switch is controlled by the "Master Avionics" toggle switch on the instrument panel. A red lamp on the instrument panel is lit while the Master Avionic switch is OFF.

Notice

In case of failure to the Avionics Electronic Switch, one can disconnect the two plugs from the Electronic switch and connect them to each other.

A 7A capable always on Aux Outlet is provided under and behind the center control bracket.  A complete power wiring diagram is provided in this POH (see Appendix 11.2).

Rev. B.1

8.11 FLIGHT VACUUM SYSTEM

The flight data is manipulated and displayed by the "Dynon D-10 EFIS".

The D-10 is fed from three pressure sources:

- Static Pressure,

- Dynamic (Pitot) Pressure and

- AOA Pressure.

The Pitot pressure and the Static pressure are also fed to conventional High Sensitive Altimeter and ASI which used as back-up to the D-10.

Fig 8.12 – Flight Vacuum System Diagram

##### Rev. B.2

##### This page left Blank intentionally

##### Rev. B.1

##### 9. AIRPLANE HANDLING, SERVICE & MAINTENANCE

##### 9.1 Daily Inspection

| Location | Item to be checked | Condition / Operation | remarks |
| --- | --- | --- | --- |
| Cockpit |  |  |  |
| 1 | Control Lock | Remove |  |
| 2 | Battery Switch | ON |  |
| 3 | Fuel Quantity | CHECK |  |
| 4 | Lights | CHECK |  |
| 5 | All Switches | OFF |  |
| 6 | Flaps | Extend | Check Flaps Position Indicator |
| 7 | Trim | Operate all directions | Check Trim Position Indicators |
| 8 | Canopy | Smooth movement |  |
| 9 | Canopy Lock | Condition |  |
| Left Main Gear |  |  |  |
| 1 | Tire | Condition / Tread |  |
| 2 | Chocks | Remove |  |
| 3 | Brake Pads | Condition |  |
| 4 | Brake Line | No Chafing |  |
| Left Wing |  |  |  |
| 1 | Leading Edge | Smooth, No Damage, Clean |  |
| 2 | Upper / Lower surface | Smooth, No buckling / distortion |  |
| 3 | Fuel Quantity | Adequate For Flight, Cap Secured!!! |  |
| 4 | Tank Sump | Drain, No leak |  |
|  |  |  | Rev. B.2 |
| 5 | Pitot | Clean, no Damage and not Blocked |  |
| 6 | Wing Tip | No Damage, No Cracks, Paint and Pos Light and Strobe |  |
| 7 | Left Aileron | Condition, Free Movement | Check that there are no any foreign Objects between aileron and wing |
| 8 | Left Flap | Condition, Flap Actuator | Check piano hinge |
| Left Fuselage |  |  |  |
| 1 | Static Port | Clean and not blocked |  |
| Tail Assembly |  |  |  |
| 1 | Horizontal Stabilizer | Condition, No damage to leading edge |  |
| 2 | Vertical Stabilizer | Condition, No damage to leading edge |  |
| 3 | Elevator/Rudder | Free motion, No rubbing |  |
| 4 | Trim Tab | Condition |  |
| 5 | Rudder Cable | Secure, No Bending of cable to fitting |  |
| Right Fuselage |  |  |  |
| 1 | Static Port | Clean and not blocked |  |
| Right Wing |  |  |  |
| 1 | Right Flap | Condition, Flap Actuator | Check piano hinge |
|  |  |  | Rev. B.2 |
| 2 | Right Aileron | Condition, Free Movement | Check that there are no any foreign Objects between aileron and wing |
| 3 | Wing Tip | No Damage, No Cracks, Paint and Pos Light and Strobe |  |
| 4 | Tank Sump | Drain, No leak |  |
| 5 | Fuel Quantity | Adequate For Flight, Cap Secured!!! |  |
| 6 | Upper / Lower surface | Smooth, No buckling / distortion |  |
| 7 | Leading Edge | Smooth, No Damage, Clean |  |
| Right Main Gear |  |  |  |
| 1 | Tire | Condition / Tread |  |
| 2 | Chocks | Removed |  |
| 3 | Brake Pads | Condition |  |
| 4 | Brake Line | No Chafing |  |
| Right Nose Area |  |  |  |
| 1 | Oil Quantity | 7Quarts minimum |  |
| 2 | Dip Stick | Secure Not too tight! |  |
| 3 | Inspection Door | Close / secure |  |
| Nose Front |  |  |  |
|  | Propeller | Blades Smooth, No nicks |  |
|  | Spinner | Secure, no cracks at attach screws |  |
| Left Nose Area |  |  |  |
|  | Cowling | Secure |  |
|  | NACA Port | No obstruction, No birds nests |  |

Rev. B.1

9.2 50 Hours Inspection

The following list shall be performed, in addition to the daily inspection list, every 50 hours or every six (6) months whichever comes first.

- Drain oil sump with oil hot. Send sample for analysis (see Lycoming Service Letter No. 171).

- Replace oil filter. Cut open &inspect (The filter paper).

- Add 7 to 8 Quarts of Aircraft grade oil according to Lycoming Service Instruction No.   1014M

- Inspect & clean suction oil screen.

- Check & record brake fluid level.

- Check condition and integrity of:

- Fuel & oil hoses.

- Spark Plugs and Ignition system.

- Magneto P-lead & mounting bolts.

- Exhaust system & attachment hardware.

- Cylinders – check for oil leak at rocker box covers, and check for signs of overheating (burned paint).

- Baffling / plenum.

- Firewall forward wiring.

- Engine mounting bolts.

- Firewall seals.

- Cowling hinge eyes.

- Inspect & lubricate:

- Throttle, Mixture & Prop linkages.

- Alternate air door & control.

- Check alternator belt condition & tension.

- Check tires for wear and correct, rotate – replace as necessary.

- On test flight, log engine data.

Rev. B.2

9.3 100 Hours Inspection

##### Engine Section

- Preparations

Remove and clean engine cowling and baffles: Inspect for cracks, wash engine.

- Hot engine compression

perform a hot engine differential compression check:

cylinder reading:
1.                2.               3.                4.

3. Lubricating system

a. drain sump and change oil filter

b. remove pressure and suction screens, check for metal particles

c. clean and inspect screens, reinstall and safety screens

d. check engine for oil leaks (note and correct)

e. inspect condition of oil cooler

f. service engine with recommended lubricating oil (refer to Lycoming specification 301E and service instruction 1014 or T.C.M service manual

4. Ignition and Electrical Systems

a. inspect spark plugs, replace or clean, and Adjust gaps.

b. inspect ignition harness for general condition, free from fraying or chaffing.

c. Inspect magnetos and points: check magneto timing: check distributor block for erosion or cracks.

d. inspect ignition timing in accordance with Lycoming SI No.1437

5. Electrical system

a. inspect battery for security, and vent for obstruction.

b. inspect generator or alternator and accessories.

c. inspect electrical components and wiring.

d. inspect starter and starter drive: lubricate starter drive.

6. Fuel system

a. inspect fuel injection system, clean screens, and injector nozzles (refer to Bendix service manual or T.C.M. service manual).

b. check power boost system for proper operation and seal for leaks (M20E, F G J).

c. remove, clean and inspect dry-air filter.

d. inspect air induction system and alternate air valve

e. inspect fuel selector valve for operation and proper pointer indication.

f. operate boost pump, check pressure and all lines for leaks.

g. Clean Gascolator screen.

h. Check fuel pressure.

Rev. B.1

7. Exhaust System - remove heater jacket and inspect exhaust system for leaks and cracks. Remove exhaust cavities, inspect area.

8. Firewall - Inspect firewall for proper sealing and freedom form cracks.

10.  Engine Mount - Inspect tubular engine mount for cracks, bolts and rubber mounts for security.

11.  Engine Controls - Lubricate engine controls and inspect for security, full travel, free movement.

12. Spinner - Remove propeller's spinner and check for cracks and general condition.

13. Propeller - Inspect propeller's hub for grease leakage, check hub bolts and mounting bolts for proper torque, inspect blades for cracks nicks, and dents, lubricate as needed (refer to appropriate manufacturers, handbook.

14. Reinstall Spinner - Reinstall spinner, check for correct interference fit with prop. Cylinder – shim with Teflon tape a/r.

##### Airframe Section

1. General Condition - Inspect exterior and interior of aircraft for general condition, collision damage, dents and loose rivets.

2. Lower Longerons - Inspect tubular structure lower longerons.

3. Control surfaces - Inspect control surfaces for security of attachment, proper rigging, free movement, collision damage, dents.

4.  Flight Controls Lubrication Lubricate flight control system guide L hinge points, rod end bearing, and bell cranks.

5. Fuselage / Wings / Empennage - Inspect all wing, fuselage, and empennage during drain holes for obstruction.

6.  Trim - Inspect empennage trim system for proper operation and rigging.

7.  Flaps - Inspect flap system for proper operation and rigging, lubricate.

8. Flight Instruments (ASI, Altimeter & Dynon) - Inspect flight instruments, filters, and vacuum system for proper operation, marking, and condition, clean vacuum air filter.

Rev. B.1

9. Electric - Cabin - Inspect cabin lights, circuit – breakers, and electrical components for proper operation.

10. Wings interior - Inspect wing interior in fuel tank area for fuel leaks, fuel tank vents for obstruction, and fuel filler caps for security and proper operation.

11.  Canopy - Inspect Canopy for condition (cracks, crazing scratches & distortion), proper operation and sealing.

12.  Seats & Harnesses - Inspect seats, seat belts and shoulder harnesses for security, proper operation, and condition

13.  Magnetic Compass - Inspect compass deviation card for proper indication and compensation.

14.  Avionics - Inspect Avionics equipment for proper installation and operation.

##### LANDING GEAR

Raise aircraft on jacks -

1.  Breaks - Inspect breaks, hydraulic break cylinders, and hydraulic system for leaks and general condition.

2. Wheel Inspection - Remove wheels, inspect, repack, reinstall, and safety. Lubricate brake guide pins using silicone base lubricant. Check wheels for free rotation and proper brake action.

D. POST-INSPECTATION OPERATION CHECK

1.  Propeller Governor - Check propeller governor operation with engine running at 2000 rpm and pitch control at low pitch (high rpm) when propeller control is pulled out to high pitch (low rpm),  engine speed should decrease at least 500 rpm.

2.  Engine Controls - Check ease of operation for all engine controls with engine running.

3. Alternator Indications - Check alternator output indication.

4. Oil Pressure - Check oil pressure indication

5.  Fuel Pressure - Check fuel pressure indication

6. Fuel Quantity - Check fuel quantity gauges indication and warning light.

Rev. B.1

7. Cylinder Head Temperature - Check cylinder head temperature indication.

8.  EGT Gauge - Check EGT gauge operation.

9.  Oil Temperature - Check oil temperature indication.

10. Engine Idle RPM - Check idle rpm idle mixture and idle cutoff.

11.  Propeller Pitch Control - Check propeller pitch through range.

13. Magnetos Drop - Check magneto drop and ground.

14.  Cabin Lights - Check cabin and panel lights.

15.  Avionics - Check radio and Avionics operation.

16.  Fuel Selector Valve - Check fuel selector valve operation.

17. Flap position Indicator - Check flap position indicator.

18.  Trim Pos. Indicator - Check trim position indicator.

19. Breaks Operation - Check brake operation.

##### Rev. B.1

##### 9.4 Annual condition inspection

This section describes the annual inspection requirements. The following list will be print out as a separate document to be performed by one of the Primary Builders of this aircraft, or by a licensed AP.

Each checked item should be recorded.

After completion of the annual inspection this report should be kept in the maintenance file to be presented, if required, to the authorities.

Engine and Propeller should be overhauled based of "ON-Condition" basis.

Rev. C.1

|  | Annual Condition Inspection |  |
| --- | --- | --- |
| MAKE: | RV-8A |  |  |
| REGISTRATION #: | 4X-OAA | SERIAL #: | 80295 |
|  |  | Date: |  |
|  |  | Airframe Hours: |  |
|  |  | Engine Hours: |  |
|  |  | Propeller Hours: |  |
| Performed By: | Name: |  | Signature: |  |

Preperations - Periodical Replacement Consumables

| Item | Mfr. P/N | Activity | Replace every: (Hours) | Next Replacement (Hobbs) |
| --- | --- | --- | --- | --- |
| Oil |  |  | 50 |  |
| Oil Filter |  |  |  |  |
| Spark Plugs |  |  |  |  |
| ELT Batteries |  |  |  |  |
| ELT Remote Batteries |  |  |  |  |
| Air Filter |  |  |  |  |
| Brakes |  |  |  |  |
| Tires/Tubes |  |  |  |  |
| Wheel Bearing Grease |  |  |  |  |

Time Limited Items - Change per:

| Item | Last Replaced | Next Total Time to replace | Next HOBBS to replace |
| --- | --- | --- | --- |
| ELT Batteries (Replace every 1 year) |  |  |  |
| ELT Remote Battery (Replace every 2 years) |  |  |  |
| Transponder Inspection & Certification |  |  |  |

Rev C.1

A. PROPELLER GROUP

- [....] Remove spinner, inspect it  and back plate for no cracks and corrosion....

- [....] Inspect blades for nicks and cracks....

- [....] Check for grease and oil leaks....

- [....] Check spinner mounting brackets....

- [....] Check propeller mounting bolts and safety....

- [....] Inspect hub parts for cracks and corrosion....

- [....] Reinstall Spinner...

B. ENGINE GROUP

- [....] Remove engine cowls....

- [....] Clean and check cowling for cracks, distortion and loose or missing fasteners....

- [....] Drain engine  oil sump...

- [....] Remove, inspect, and replace oil filter…

- [....] Cut open oil filter, inspect for particles...

- [....] Check oil temp and oil pressure senders for leaks and security....

- [....] Check oil lines and fittings for leaks, chafing security, dents and cracks....

- [....] Clean and check oil cooler fins....

- [....] Fill engine with oil per lubrication chart...

- [....] Clean engine....

- [....] Check condition of spark plugs, adjust gap (0.018" / 0.46mm)....

- [....] Check ignition harness and insulators....

- [....] Conduct a compression check: #1 ___/80,  #2 ___/80,  #3 ___/80,  #4  ___/80

- [....] Check magnetos timing…

- [....] Reinstall Spark Plugs (Rotate position) apply anti-seize and torque to 35 ft/lbs....

- [....] Remove air filter and clean....

- [....] Check intake seal for leaks and clamps for tightness....

Rev C.1

- [....] Inspect condition of fuel lines....

- [....] Check fuel system for leaks.....

- [....] Check engine controls – throttle and mixture…

- [....] Inspect exhaust stacks, connections, gaskets and retorque mounting nuts....

- [....] Inspect heat exchange and baffles....

- [....] Check breather tube for obstructions and security....

- [....] Check crankcase for cracks, leaks, security of bolts....

- [....] Check engine mounts for cracks and loose mountings.......

- [....] Check firewall seals....

- [....] Remove Alternator’s drive belt and turn the alternator’s rotor to check    condition of bearings for abnormal noise or roughness...

- [....] Check condition of the drive belt, replace if required, attach the drive belt and check for correct tension....

- [....] 5 Year or 1000 hour intervals – Remove field brush assembly and inspect brushes for excess wear. Replace brush assembly if brushes extend less than ¼” from edge of brush holder case…

- [....] Check condition of starter....

- [....] Check fluid in brake reservoir....

- [....] Lubricate all controls....

- [....] Reinstall engine cowl....

Rev. C.1

C. CABIN GROUP

- [....] Inspect canopy and windows....

- [....] Check upholstery for tears....

- [....] Check seats, seat belts, shoulder straps....

- [....] Check trim operation...

- [....] Check rudder pedals....

- [....] Check electric fuel pump for operation.....

- [....] Check fuel filter….

- [....] Check control stick, systems and connection.....

- [....] Check landing, Taxi, Strobe, NAV, cabin, and instrument lights...

- [ ] Check Dimmers functioning…

- [....] Recalibrate the Flap Position Indicator…

- [....] Check instruments, lines and attachments....

- [....] Check operation of fuel selector valve....

- [....] Replace ELT batteries (Duracell MN1300 for the ELT unit and Duracell DL1/3NB for the Remote unit). Operate the ELT by the remote switch, for three seconds, and verify reception by the Control Tower

(This test must be performed during the first 5 minutes of the round hour and for no longer then 3 seconds)

- [....] Check condition of heater controls....

- [....] Check condition and operation air vents....

- [....] Check all placards condition….

D. FUSELAGE AND EMPENNAGE GROUP

- [....] Remove inspection plates and panels...

- [....] Check electronic installations....

- [....] Check bulkheads and stringers for damage...

- [....] Check antenna mounts and wiring....

- [....] Check fuel lines and valves....

Rev C.1

- [....] Check vertical fin and rudder surfaces....

- [....] Check rudder horn and attachment....

- [....] Check vertical fin attachments....

- [....] Check rudder bolts for wear...

- [....] Check horizontal stabilizer and elevators...

- [....] Check horizontal stabilizer attachment...

- [....] Check elevator trim servo for wear and operation…

- [....] Check elevator horn...

- [....] Check elevator bolts for wear...

- [....] Check elevator bell cranks and controls....

- [....] Lubricate all bearings as needed.....

- [....] Reinstall inspection plates and panels....

- [....] Check Radios and Avionics antennas condition…

- [....] Check integrity of the 4X- *** letters….

E. WING GROUP

- [....] Remove inspection plates...

- [....] Check surfaces and tip for damage and loose rivets and condition of walkways....

- [....] Check aileron mounts and attachments....

- [....] Check aileron bell-crank and control tubes....

- [....] Check flaps and attachment for damages....

- [....] Check all wing attachment bolts....

- [....] Check fuel tanks and lines for leaks...

- [....] Check fuel tank vents....

- [....] Reinstall inspection plates....

- [....] Operate and check Landing and Taxi lights. Check lenses condition (no cracks no scratches) and transparency….

Rev C.1

- [....] Operate and check Position lights (including the rudder's white light) condition. Check lenses condition (no cracks no scratches) and transparency….

- [....] Operate and check Strobe-Lights condition. Check lenses condition (no cracks no scratches) and transparency….

F. LANDING GEAR GROUP

- [....] Check nose gear travel and damper tightness....

- [....] Check main gear attachments...

- [....] Check tires for cuts and wear....

- [....] Remove wheel, clean, and repack bearings...

- [....] Check wheels for cracks, corrosion and broken bolts....

- [....] Check tire pressure....

- [....] Check brake lining and disc....

- [....] Check brake lines....

G. OPERATIONAL INSPECTION

- [....] Check fuel pump and fuel tank selector....

- [....] Check fuel pressure....

- [....] Check oil pressure and temperature....

- [....] Check alternator output....

- [....] Check manifold pressure....

- [....] Check Cabin heat operation....

- [....] Check throttle and mixture operation....

- [....] Check propeller smoothness....

- [....] Check electronic equipment operation....

Rev C.1

H. Documentation

1.  	[....] Perform Aircraft weighting, calculate and fill a W&B report....

2.  [....] Place entry of the Annual Inspection in the Aircraft's Log Book....

3.  [....] Place entry of the Annual Inspection in the engine's Log Book....

4.  [....] Place entry of the Annual Inspection in the propeller's Log Book....

I. Known problem areas – Must be checked carefully and fixed if and as required:

- Smoking rivets on forward bottom skin

- Chafing brake lines on gear leg fairing and beneath wheel pant

- Chaffing of wheel on wheel pant

- Fretting corrosion at gear leg fairing intersection

- Corrosion of exposed rod end bearings

- Rudder contacting elevator roots in flight (dynamic clearance less than static clearance!)

NOTES: ……………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………………

Rev. B.2

10. Reserved For Additional Data

This page left Blank intentionally

Rev. B.1

11. APPENDIXES

11.1 Flight and Power Plant Operations Data

- Density Altitude vs. Temperature vs. Pressure Altitude

- Take-Off Cross-Wind Calculation

Rev. B.2

- Pre-Flight Passenger Briefing

(This paragraph is written in Hebrew for the convenience of the pilot. A copy of this text is printed and been carried in the passenger cabin)

תדריך לנוסע

(על הטייס חלה חובה לקרוא לנוסע לפני ביצוע כל טיסה עם נוסע ע"מ ליידעו על אופיו המיוחד של המטוס)

- מטוס זה הוא מטוס ניסיוני שאינו בנוי ואינו נבדק עפ"י כללי התעופה המסחרית.

- אין לעשן בתוך המטוס ובסביבתו.

- הכניסה לתא המטוס מצד שמאל. אין לדרוך על משטחי המדפים אלא רק על הפסים השחורים בשורש הכנף.

- יש לחגור חגורות בטיחות בכל מהלך הטיסה.

- משדר מיקום בחירום נמצא בתא מטען אחורי.

- (בטיסה מעל הים – ציוד הישרדות במים נמצא בתא מטען אחורי).

- יש לוודא כי כל הציוד האישי המוחזק בידי הנוסע מאובטח במהלך כל הטיסה.

Rev. B.1

- POWER PLANT LIMITATIONS

The following limitations and gauges markings are for the Lycoming IO-360-M1B1

| Engine Speed (RPM) |  |  |
| --- | --- | --- |
|  | Max. - Red line | 2700 |
|  | Green arc | 500 to 2700 |
| Oil Temperature (Deg. F) |  |  |
|  | Max. | 245 |
|  | Normal | 180 |
|  | Green arc | 140 to 245 |
|  | Minimum for continuous operation - Red line | 140 |
| CHT - Cylinder Head Temperature (Deg. F) |  |  |
|  | Max. - Red line | 500 |
|  | 75% power cruise (Recommend max.) | 435 |
|  | Economy cruise (Recommended maximum) | 400 |
|  | Green arc | 150 to 500 |
|  | Recommended minimum for max. engine life | 150 |
| Oil pressure (psi) |  |  |
|  | Maximum (start, warm-up, taxi and takeoff) – Red line | 115 |
|  | Maximum (normal operations) | 95 |
|  | Minimum (normal operations) | 55 |
|  | Green arc | 55 to 95 |
|  | Yellow arc | 25 to 55 |
|  | Minimum (idle) – Red line | 25 |
|  |  | Rev. B.1 |
| Oil sump capacity (US Qts) |  |  |
|  | Maximum | 8 |
|  | Minimum safe quantity | 3 |
| Fuel pressure (at injector inlet) (psi) |  |  |
|  | Maximum – red line | 45 |
|  | Green arc | 14 to 45 |
|  | Minimum – Red line | 14 |
| Fuel Level (gal.) |  |  |
|  | Minimum per tank – Red line + Red Ind. Light | 5 |

Starter cranking is limited to six 10 second cranking cycles with 20 second cool down between cranking attempts, then 30 minutes cooling.

Rev. B.1

- Power Setting & Fuel Consumption Table

In order to get out of the engine the rated power and the fuel consumption as follow, manifold pressure should be set as per the table below:

| Press. Alt. (x1000 ft) | Std. Alt. Temp. (( C) | Rated Power = 99 HP (55%) | 117 HP (65%) | 135 HP (75%) |
| --- | --- | --- | --- | --- |
|  |  | Fuel consumption = 7.4 gph | 8.8 | 10 |
|  |  | RPM & MAN. PRESS. For the above setting |
|  |  | 2100 | 2200 | 2300 | 2400 | 2100 | 2200 | 2300 | 2400 | 2200 | 2300 | 2400 |
| SL | 15 | 20.9 | 20.3 | 19.8 | 19.3 | 23.3 | 22.7 | 22.1 | 21.5 | 25.1 | 24.5 | 23.9 |
| 1 | 13 | 20.7 | 20.1 | 19.6 | 19.1 | 23.1 | 22.4 | 21.8 | 21.3 | 24.8 | 24.2 | 23.6 |
| 2 | 11 | 20.4 | 19.8 | 19.3 | 18.8 | 22.8 | 22.1 | 21.6 | 21.0 | 24.6 | 24.0 | 23.4 |
| 3 | 9 | 20.2 | 19.6 | 19.1 | 18.6 | 22.5 | 21.9 | 21.3 | 20.8 | 24.3 | 23.7 | 23.2 |
| 4 | 7 | 19.9 | 19.3 | 18.9 | 18.4 | 22.3 | 21.6 | 21.1 | 20.6 | 24.0 | 23.5 | 22.9 |
| 5 | 5 | 19.7 | 19.1 | 18.7 | 18.2 | 22.0 | 21.4 | 20.9 | 20.3 | 23.8 | 23.2 | 22.7 |
| 6 | 3 | 19.5 | 18.9 | 18.4 | 18.0 | 21.8 | 21.1 | 20.6 | 20.1 | --- | 23.0 | 22.5 |
| 7 | 1 | 19.3 | 18.7 | 18.2 | 17.8 | 21.5 | 20.9 | 20.4 | 19.9 | --- | --- | 22.2 |
| 8 | -1 | 19.0 | 18.4 | 18.0 | 17.6 | 21.3 | 20.7 | 20.2 | 19.7 | --- | --- | 22.0 |
| 9 | -3 | 18.8 | 18.2 | 17.8 | 17.4 | --- | 20.4 | 20.0 | 19.5 | --- | --- | 21.8 |
| 10 | -5 | 18.6 | 18.0 | 17.6 | 17.2 | --- | --- | 19.8 | 19.3 | --- | --- | 21.5 |
| 11 | -7 | 18.4 | 17.8 | 17.4 | 17.0 | --- | --- | --- | 19.1 | --- | --- | 21.2 |
| 12 | -9 | 18.2 | 17.6 | 17.2 | 16.8 | --- | --- | --- | 18.9 | --- | --- | 21.0 |
| 13 | -11 | --- | 17.4 | 17.0 | 16.7 | --- | --- | --- | 18.7 | --- | --- | 20.7 |
| 14 | -13 | --- | --- | 16.8 | 16.5 | --- | --- | --- | 18.5 | --- | --- | 20.5 |
| 15 | -15 | --- | --- | 16.6 | 16.3 | --- | --- | --- | 18.3 | --- | --- | 20.3 |

To maintain constant power, correct manifold pressure approximately 0.17" Hg for each 5.6( C. variation in air temperature from standard altitude temperature.  Add manifold pressure for air temperatures above standard; subtract for temperatures below standard.

Rev. B.2.

This page left Blank intentionally

11.2 Electrical System Diagram                                                                                                          Rev B.2

  - Page 2 - Firewall forward

  - Page 3 - Battery Compartment                                                                                             Rev B.2

  - Page 4 - Electrical Buses & Circuits Breakers                                                                        Rev B.2

  - Page 5 – Instruments Panel                                                                                               Rev B.2

  - Page 6a – Left Wing                                                                                                                 Rev B.2

  - Page 6b – Right Wing                                                                                                              Rev B.2

G. Page 6c – Tail & Fuselage                                                                                                                     Rev B.2

  - Page 7 – Trim System								Rev B.2

  - Page 8 – Sub Panels							Rev B.2

  - Page 9a – Left Lower Console								Rev B.2

  - Page 9b – Right Lower Console								Rev B.2

K. Page 9c - Part of Instruments Panel								Rev C4

L. Page 10 - Sticks Wiring								Rev B.2

Rev B.2

This page left Blank intentionally

Rev. B.2

11.3 ID Placard

Rev. C.2

11.4 Equipment List

| # | Section | Item | Mfr. | Mfr P/N / Model | Qty. |
| --- | --- | --- | --- | --- | --- |
| A | Avionics & Flight Instruments |  |  |  |  |
|  | A1 | EFIS - Flight Data | Dynon Avionics | D-10 | 1 |
|  | A2 | Remote Digital Compass | Dynon Avionics | EDC-D10 | 1 |
|  | A3 | Pitot Probe | Dynon Avionics | 100141-000 | 1 |
|  | A4 | OAT Probe | Dynon Avionics | OAT | 1 |
|  | A5 | Radio | Icom | A-200 | 1 |
|  | A6 | COM Antenna | RAMI | AV-17 | 1 |
|  | A7 | Multisystem Avionics | Garmin | GNS-430 | 1 |
|  | A8 | Transponder | Narco Avionics | AT-155 | 1 |
|  | A9 | Transponder Antenna | RAMI | AV-22 | 1 |
|  | A10 | ELT | AMERI-KING | AK-450 | 1 |
|  | A11 | Audio Panel | PS | PS465 | 1 |
|  | A12 | ASI | UMA | 16-311-241D | 1 |
|  | A13 | Altimeter | Van's | IF BG-3E | 1 |
|  | A14 | Accelerometer | Van's | IF BJ10-2 | 1 |
|  | A15 | Encoder (Blind) | Ameri-King | AK-350 | 1 |
|  | A16 | Compass Panel Mount | Van's | IF CM-13L | 1 |
|  | A17 | GPS | Garmin | Area-500 | 1 |

Rev. B.2

| E | Engine Gauges |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
|  | E1 | RPM (Tachometer) | Van's | IE VTACH3500 | 1 |
|  | E2 | Tachometer Transducer | Van's | IE VTACHGEN 2 | 1 |
|  | E3 | Manifold Pressure | Van's | IE VMP35 | 1 |
|  | E4 | Oil Temp | Van's | IE VOT250 | 1 |
|  | E5 | Oil Temp Probe | Van's | IE P-120 | 1 |
|  | E6 | Oil Pressure | Van's | IE VOP100 | 1 |
|  | E7 | Oil Pressure Transducer | Van's | IE 411K | 1 |
|  | E8 | CHT | Van's | IE VCHT600 | 1 |
|  | E9 | EGT | Van's | IE VEGT1600 | 1 |
|  | E10 | Fuel Pressure | UMA | N04-262U-060P-000 | 1 |
|  | E11 | Fuel Pressure Sender | UMA | N1EU70G | 1 |
|  | E12 | Fuel Level | Van's | IE VFL15 | 2 |
|  | E13 | Fuel Level Sender Left | Van's | IE F-385B | 1 |
|  | E14 | Fuel Level Sender Right | Van's | IE F-385C | 1 |
|  | E15 | Ammeter | Van's | IE VAM40 | 1 |
|  | E16 | Voltmeter | Van's | IE VV16 | 1 |
| S | Systems |  |  |  |  |
|  | S1 | Two Place trim Mixer | ARIEL ATE | 307049-0100 | 1 |
|  | S2 | Electronic Avionic Switch | ARIEL ATE | 308049-0100 | 1 |
|  | S3 | Flap Position Indicator | ARIEL ATE | 181059-0100 | 1 |
|  | S4 | Trim Position Indicator | RAC | RP3 | 3 |
|  | S5 | Strobe Lights Power Supply | WHELEN | HDACF | 1 |
|  | S6 | Wing Tip Strobe/Pos RED | WHELEN | A600PR14 | 1 |
|  | S7 | Wing Tip Strobe/Pos GRN | WHELEN | A600PG14 | 1 |
|  | S8 | Tail Pos WHT | WHELEN | A500AH14 | 1 |
|  | S9 | Leading Edge Lights (kit of two) | Van's | LL HID-DW50 | 1 |

Rev. B.2

11.5 Load Factor Limitations

Rev. B.2

11.6 Engine out – Glide performance

The best L/D speed is 75 Kt.

The following graph illustrate distance vs. altitude no wind, performance.

11.7 Nose Gear Maximum Loading   	Rev. C.3

In March, 2005, Van’s Aircraft issued a service letter describing the development and

revisions made to the nose gear legs used on all two place, tricycle RVs .

This service letter went on to describe the most recent revisions in the nose gear leg

design, a shortened gear leg axle and shorter fork. This version of the nose gear leg and

fork have been shipped as standard components in Van’s kits since February, 2005. As

of October, 2007, there have been no reported nose gear incidents involving this

combination of leg and fork.

On June 21, 2007, The NTSB released a Structures Study of the pre-shortened nose gear

leg/fork combination. This report concluded that, though the nose gear

strut has sufficient strength to perform its intended function, mechanical factors and

piloting technique that reduced the nose gear leg strut to ground clearance increased the

likelihood of an incident.

In light of the absence of incidents involving the current, shortened nose leg/fork

combination and the results of the NTSB Structures Study, Van’s Aircraft, Inc. issued

Mandatory Service Bulletin 07-11-09. This SB has been performed on RV8A S/N 80295 (4X-OAA). The upgraded leg/fork combination is notably lighter than the previous version and allows an additional inch of clearance between the fork/axle assembly and runway surface.

The following graph illustrates the limits of nose gear loading as a function of A/C gross weight and Centre of Gravity location and it should be carefully maintained on unpaved runways. (On paved runways the gross weight limit is increased to 1900lb but the Weight on Nose Wheel (lb) should not be chainged)!